Determination of the  Worst Peak Output Voltage in a Linear Time Invariant Circuit   based on the Step Response
Determination of the
Worst Peak Output
Voltage in a Linear
Time Invariant Circuit
based on the Step Response

---
Module
under
Test
(internal nodes)
nodes
to be
analyzed
In
Out
Hypothesis:
Input is bounded Lmin <= In <= Lmax
Module is causal, LINEAR and time-invariant

---
#* s0 sn0
#* x -->(+)------------------+----->[*n0/d0]---->(+)--> y
#* | __|__ |
#* | | | |
#* | |Delay| |
#* | |_____| |
#* | sd1 | s1 sn1 |
#* (+)<----[*-d1/d0]<---+----->[*n1/d0]---->(+)
#* | __|__ |
#* | | | |
#* | |Delay| |
#* | |_____| |
#* | sd2 | s2 sn2 |
#* (+)-----[*-d2/d0]<---+----->[*n2/d0]-----(+)
#* | __|__ |
#* | | | |
#* | |Delay| |
#* | |_____| |
#* | sd3 | s3 sn3 |
#* +------[*-d3/d0]<---+----->[*n3/d0]------+
#*
#* feedback path feedforward path
We will apply the method
to an example:
the Output of this
High Pass IIR Analog Filter
Lmin = 0.0
Lmax = 1.0

---
Local Extrema of the IIR Transfer Function
NAPA netlist
header <napatool.hdr>
title “transfer function of IIR filter”
fs 48.0e3
ivar npts POWEROF2(20)
directive REPEAT 25
node in noise 0.0 1.0
node out generator hpf3 <iir> "f3.dat" in
tool tf "tf.out" in 1.0 out 1.0 5.0e3 npts // transfer function
terminate TOOL_INDEX >= 1
file “f3.dat”
## IIR filter, High Pass.
# numerator denominator
0 -0.986961 1.000000
1 2.960880 -2.973750
2 -2.960880 2.947840
3 0.986961 -0.974089

---
NAPA cell produced by previous netlist: “hpf3_0.gen”
cell interface $y $dummy $x
declare (analog) $x
# feedforward path coefficients
dvar $n0 -9.86961000000000e-001
dvar $n1 2.96088000000000e+000
dvar $n2 -2.96088000000000e+000
dvar $n3 9.86961000000000e-001
# feedback path coefficients
dvar $d1 -2.97375000000000e+000
dvar $d2 2.94784000000000e+000
dvar $d3 -9.74089000000000e-001
# signal path
node $s1 delay $s0
node $s2 delay $s1
node $s3 delay $s2
node $sd1 gain -$d1 $s1
node $sd2 gain -$d2 $s2
node $sd3 gain -$d3 $s3
node $sn0 gain $n0 $s0
node $sn1 gain $n1 $s1
node $sn2 gain $n2 $s2
node $sn3 gain $n3 $s3
node $s0 sum $sd1 $sd2 $sd3 $x
node $y sum $sn0 $sn1 $sn2 $sn3

---
file “tf.out”
IIR Filter Transfer Function
-120
-100
-80
-60
-40
-20
0
0.01
0.1
1
10
100
1000
10000
Log(freq)
dB

---
We will use this IIR filter to show the method of determination
of the worst case of peak.
Apply a step function Lmax
        Lmin
Use the step response to compute the worst case of peak
using the theorem of superposition for linear systems

---
IIR Filter Step Response
NAPA netlist
header <napatool.hdr>
fs 48.0e3
title “Step Response of IIR Filter”
node in step 0.0 1.0 1.0e-6
node out generator hpf3 <iir> "f3.dat" in
node stb iuser stable out 10 1.0e-6 // check for signal stabilization
output "resp.out" in out // step response
terminate (LOOP_INDEX >= 5000) || stb

---
file “resp.out”
IIR Filter Step Response
-1
-0.5
0
0.5
1
0
0.005
0.01
0.015
0.02
0.025
0.03
0.035
0.04
0.045
current time
out

---
Local Extrema of the IIR Filter Step Response
NAPA netlist
header <napatool.hdr>
fs 48.0e3
title “Local Extrema of the IIR Filter Step Response”
node in step 0.0 1.0 1.0e-6
node out generator hpf3 <iir> "f3.dat" in
node stb iuser stable out 10 1.0e-6 // check for signal stabilization
output "resp.out" in out // step response
post extrema “ext.out" 0 2 (short) // list of extrema
terminate (LOOP_INDEX >= 5000) || stb

---
Local Extrema of the IIR Filter Step Response
-1
-0.5
0
0.5
1
0
0.005
0.01
0.015
0.02
0.025
0.03
0.035
0.04
0.045
current time
out
4
3
2
1
time	voltage
5	0.00000000e+0 0.00000000e+0 init
4	2.08333333e-5 -9.86961000e-1 min
3	2.58333333e-3 2.46762100e-1 max
2	7.81250000e-3 -3.70431800e-2 min
1	4.31250000e-2 -2.73156600e-5 dc
5

---
Method A
- Indirect Method -
Use Time Position of Local Extrema
of the IIR Filter Step Response
to build activations leading to
the Worst Case Peak voltage.

---
Method A: Use Time Position of Local Extrema of the IIR Filter Step Response
input
Build an activation in
such a way that all
maximums occur
at the same time.
Superposition of maximums

---
Method A: Use Time Position of Local Extrema of the IIR Filter Step Response
input signal to build worst case of peak
Temporal inversion
-0.5
0
0.5
1
1.5
0
0.005
0.01
0.015
0.02
0.025
0.03
0.035
time
4
3
2
5
1
4
3
2
5
1

---
Method A: Use Time Position of Local Extrema of the IIR Filter Step Response
NAPA netlist
header <napatool.hdr>
fs 48.0e3
title “Build activation for Worst Case of Peak of IIR filter”
debug WCPK_PWL
node in step 0.0 1.0 1.0e-6
node out generator hpf3 <iir> "f3.dat" in
node stb iuser stable out 10 1.0e-6 // check for signal stabilization
output "resp.out" in out	// step response
post wcpk_pwl "wcpk_pwl.out" 0 2 // compute the 2 activations to be used
// to get this worst case of peak
terminate (LOOP_INDEX >= 5000) || stb

---
Method A: Use Time Position of Local Extrema of the IIR Filter Step Response
# time inp inm
0.000000e+0 1.0 0.0
2.372917e-2 1.0 0.0
2.375000e-2 0.0 1.0
2.895833e-2 0.0 1.0
2.897917e-2 1.0 0.0
3.152083e-2 1.0 0.0
3.154167e-2 0.0 1.0
3.158333e-2 0.0 1.0
-0.5
0
0.5
1
1.5
0
0.005
0.01
0.015
0.02
0.025
0.03
0.035
time
inp
4
3
2
5
1

---
Use Computed Activation to get the Worst Case of Peak
NAPA netlist
header <napatool.hdr>
title “Use computed PWL to get the Worst Case of Peak"
fs 48.0e3 // same sampling frequency !!!
debug PWL
node inp duser pwl "wcpk_pwl.out" TIME 1 (aperiodic)
node inm duser pwl "wcpk_pwl.out" TIME 2 (aperiodic)
node outp generator hpf3p <iir> "f3.dat" inp
node outm generator hpf3m <iir> "f3.dat" inm
node stbp iuser stable outp 100 1.0e-4
node stbm iuser stable outm 100 1.0e-4
output "worst.out" inp inm outp outm
terminate (LOOP_INDEX > 10000) || (stbm && stbp)

---
file “worst.out”
Minimum Peak Voltage of IIR Filter
-1.5
-1
-0.5
0
0.5
1
1.5
0
0.01
0.02
0.03
0.04
0.05
0.06
0.07
current time
inm
outm
Reserve some
time for
stabilization

---
file “worst.out”
Maximum Peak Voltage of IIR Filter
-1.5
-1
-0.5
0
0.5
1
1.5
0
0.01
0.02
0.03
0.04
0.05
0.06
0.07
current time
inp
outp
Reserve some
time for
stabilization

---
file “worst.out”
Minimum and Maximum Peak Voltage of IIR Filter
There is NO input signal
bounded between -1 and 1
which will produce larger
peak values!
-1.5
-1
-0.5
0
0.5
1
1.5
0
0.01
0.02
0.03
0.04
0.05
0.06
0.07
current time
outp
outm
PP: 2.541560 V

---
Method B
- Direct Method -
Use Local Extremum Voltages
of the IIR Filter Step Response
to get directly the value of the
Worst Case Peaks.

---
Method B: Use Local Extremum Voltages of the IIR Filter Step Response
Superposition of maximums
input

---
Method B: Use Local Extremum Voltages of the IIR Filter Step Response
-1
-0.5
0
0.5
1
0
0.005
0.01
0.015
0.02
0.025
0.03
0.035
0.04
0.045
current time
out
4
3
2
1
time	voltage
5	0.00000000e+0 0.00000000e+0 init
4	2.08333333e-5 -9.86961000e-1 min
3	2.58333333e-3 2.46762100e-1 max
2	7.81250000e-3 -3.70431800e-2 min
1	4.31250000e-2 -2.73156600e-5 dc
5
(1) DC = -2.731566e-5
(2) Min = -9.869610e-1 => Val = 0.000000e+0 - (-9.869610e-1) = 9.869610e-1
(3) Max = 2.467621e-1 => Val = 9.869610e-1 + ( 2.467621e-1) = 1.233723e+0
(4) Min = -3.704318e-2 => Val = 1.233723e+0 - (-3.704318e-2) = 1.270766e+0
Peak to Peak = ( 1.270766 * 2.0) - (-2.731566e-5) = 2.541560

---
Method B: Use Local Extremum Voltages of the IIR Filter Step Response
NAPA netlist
header <napatool.hdr>
fs 48.0e3
title “Direct Worst Case of Peak evaluation of IIR filter”
debug WCPK
node in step 0.0 1.0 1.0e-6
node out generator hpf3 <iir> "f3.dat" in
node stb iuser stable out 10 1.0e-6 // check for signal stabilization
output "resp.out" in out // step response
post wcpk "wcpk.out" 0 2 // compute the worst case of peak
terminate (LOOP_INDEX >= 5000) || stb

---
file “wcpk.out”
# F3_D
# (tool ) wcpk postprocessor applied on "resp.out"
# (compiler version ) NAPA V2.81
# (source file ) f3_d.mac
# (random seed ) 585223739
# (postprocessed file ) resp.out
# (postprocessed column) #1, #3
# (postprocessed tool ) output
#
# (postprocessed signal) current_time -> out
#
# [ Compute the WORST CASE OF PEAK from a Step Response ]
#
# Fri Feb 02 21:17:59 2007 by YVES LEDUC
# min_peak max_peak peak_to_peak
-1.270794e+000 1.270766e+000 2.541560e+000
# end of output file